## Slide 1: Drone-Based Inventory Management
Final Presentation

## Slide 2: Problem
Current inventory management solution
  Walk around with scanner (RFID or barcode), scan items on shelf
  Manual entry of details in Warehouse Management System (WMS)
  Cycle counting and audits
    Need to take place regularly to ensure that ground details match database
  Companies have to employ employees specifically for this purpose
  Increased cost, time taken
    Less accurate than a potential technology-based solution

## Slide 3: Solution
Use a drone with cameras to scan items
  Can be easily expanded (cost effective)
  Provides much more information (i.e. image of location)
  Requires a well-lit environment or night vision cameras

## Slide 4: DJI Ryze Tello EDU
Low cost ($129)
  Cheap to repair/replace
  Swappable batteries, can buy spares
Python API
  Stream camera feed into OpenCV
  Send movement commands
Safe
  Integrated propeller guards
  Low power/speed
Performance
  13 minute flight time
  Onboard Intel processor

## Slide 5: Programming with Tello
Tello SDK
  Connect to drone over WiFi
  Takeoff, land, move in flight
  Camera streaming
Tested in Python
  Code on our GitHub repository
  Successfully streamed camera
  Commanded drone to takeoff
Notes: Vidit

## Slide 6: Camera Calibration
Is needed to use AruCo markers to estimate distance
Estimates distortion causes by optics, allows for undistorting the image
Have completed calibration, and validated results
Notes: Niha Yendamuri

## Slide 7: AruCo Markers
Uses
  Estimate position of drone
  Identify locations in warehouse
Map locations to items
  4 markers in corners of each bay on shelf
  Each marker corresponds to integer ID
  Tuple of 4 IDs used as key in database for location of scanned items
Notes: Prabhav Gupta

## Slide 8: Barcode Scanning
Pyzbar library
  Free and open source
Scans QR codes and barcodes
  Warehouse doesn’t need to redo all their barcodes
Works with OpenCV
  Can pass in drone frames
Issues
  Resolution on drone too low

## Slide 9: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 10: Drone Power
Charging
  Use Qi receivers and charging pads to recharge drone
  Charging pads at each base station, near a shelf
  Low cost and easy to start
Remote start/stop
  "Press" the power button of the drone using a microcontroller
  Needs to be lightweight, have wireless connectivity
  Could be powered by same wireless charging circuit
Notes: Mithun

## Slide 11: Next Steps
Finish calibration
  Test with AruCo markers
  Try to fly drone using markers for guidance
  Stretch: mimic scanning routine
Start work on drone power
  Buy microcontrollers and other hardware
  Test modifications to the drone
  Stretch: precision landing on pad

## Slide 12: Future Goals
SLAM
  Localization of drone
  Mapping of warehouse
Multiple drones
  Controlling a swarm
  Shared map and positioning

## Slide 13: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning
Notes: Rahul Katre

## Slide 14: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 15: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 16: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 17: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 18: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 19: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 20: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 21: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 22: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 23: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 24: Scanning Routine
Items identified by QR codes or barcodes
Locations on shelves identified by AruCo markers
Drone sweeps across a single wall of shelves
Return to base station after scanning

## Slide 25: Warehouse Management System (WMS) Front-End Material UI Integration
Integration of Material UI
  Main pro of using this design system is due to its ease of use, flexibility, and performance
  Access to pre-built and customizable UI components that follow Google's Material design guidelines
UI interactions are compatible with Firebase

## Slide 26: Warehouse Management System (WMS)
Implemented using Firebase (NoSQL database)
Database has 2 collections:
  Mapping of location to item at location
  Mapping of item to locations where it is
Location determined by scanned AruCo markers
Made working demo that updates both collections as the drone scans
Supports standard WMS queries
Notes: Prakhar

## Slide 27: Current WMS Steps
Working on python script to test functionality of the rest API on Firebase
  API should be able to send valuable information
    Package location
    Date of item entry
    Current stock of any item
  Helpful with making sure the Machine Learning team has something to interface with
Will be migrating system to SQL using postgreSQL
  Rest API testing will still be useful after migration

## Slide 28: WMS Front-End Requirement Overview
Requirements:
  Button to start scan
  Button to end scan
  Statistics panel
  Authentication
Nice-to-have:
  Adjustable scan speed
  Adjustable scan path
Notes: Sai M

## Slide 29: WMS Front-End Requirements (cont.)
Statistics Panel
  List of products in stock w/ quantities
  Locations of products
  Changes in quantity over time (between subsequent scans)
  Date added
  Inconsistencies between drone scanning data and other data (if available)
Additional features
  Suggestions for warehouse organization and restructuring to optimize core business processes
  Cost-saving measures based on business requirements and client needs
Drone Use Statistics
  Data that indicates how, where, when, and how often the drone is being used
  Wear and tear info based on maintenance records
    Can be passed into an ML model to plan future drone usage to reduce maintenance and other drone-related costs
  Visualizations of drone usage for non-technical personnel and for marketing purposes
Notes: Shivank

## Slide 30: Django for backend framework
Native admin page with minimal setup cost
Consistent architecture for this so will be easy to divvy up tasks and maintain consistency
Model View Template Architecture (MVT)
  Models help developers to create, read, update, and delete objects (CRUD operations) in the original database. Also, they hold business logic, custom methods, properties, and other things related to data manipulation.
  The View is used to execute the business logic and interact with a model to carry data and renders a template. The view fetches data from a model. Then, it either gives each template access to specific data to be displayed, or it processes data beforehand.
  The Template is a presentation layer that handles the User Interface part completely. These are files with HTML code, which is used to render data. The contents of these files can be static or dynamic. A template is used only to present data since there’s no business logic in it.
  MVT uses data (Model), layout (Template), and logic (View)
  The framework has protection against the most common security attacks like XSS and CSRF (Cross-Site Request Forgery) attacks, SQL injections, Clickjacking, etc.
  The user authentication system of Django is also solid and manages usernames and passwords.
Django has great libraries
  Django REST framework is responsible for building application programming interfaces
Django is highly secure
  Handles encryption natively

## Slide 31: WMS Database Structure
In each WMS system has all items listed in a database; each item is given a unique product code that identifies what a specific item is.
In this system there are ID, Product code, Product name, Special instructions, Status (in progress, completed), Date, Quantity, and Actions. We can customize the database to have what we want.
This is a good way of how we can structure our SQL database, it has everything that we are looking for.

## Slide 32: Drone-Based Inventory Management
Questions
Notes: Rahul Katre